## Slide 1
Experiment1
Experiment2

## Slide 2: Experiment1
Super Edge
Edge1
(Client)
Edge2
(Server)
CPU Utilization of Edge1 &2
Iperf3 log
edge1
Iperf3 log
edge2
Data plane
Control plane
Edge1 & Edge2 keep streaming CPU utilization info through socket program over the control plane
UDP packets
Iperf3 –u –b [2, 4 , 6 ,..., 40M] –t 75
Streaming %CPU info 20 points for every bitrate parameters

## Slide 3
Chart: Experiment1 Bit rate
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40
Edge1 (sender) | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 27.2 | 28.6 | 29.4 | 27.8 | 28 | 27.4
Edge2 (Receiver) | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 27.2 | 28.6 | 29.4 | 27.7 | 28 | 27.3
Saturated point
~ 28 Mbps

## Slide 4
Chart: Experiment1 %CPU Utilisation
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40
Edge1 (sender) | 0.03299 | 0.052501 | 0.04381 | 0.048954 | 0.035296 | 0.043278 | 0.046293 | 0.042746 | 0.041504 | 0.047357 | 0.048244 | 0.05392 | 0.052501 | 0.095424 | 0.18659 | 0.17506 | 0.18162 | 0.18801 | 0.16885 | 0.19262
Edge2 (receiver) | 0.17559 | 0.33469 | 0.35154 | 0.46045 | 0.57769 | 0.66353 | 0.73093 | 0.78538 | 0.86343 | 0.91274 | 0.94856 | 0.95708 | 0.98528 | 0.99823 | 0.96985 | 0.99503 | 1 | 0.96187 | 0.97978 | 0.98812
Saturated point of Edge2
~ 28 Mbps

## Slide 5: Experiment2
Super Edge
Edge1
(Server)
Edge5
(Server)
CPU Utilization of Edge1 &2
Iperf3 log
edge1
Iperf3 log
edge5
Data plane
Control plane
UDP packets
Iperf3 –u –b [2, 4 , 6 ,..., 40M] –t 75
Streaming %CPU info 20 points for every bitrate parameters
Edge4
(Client)
Iperf3 log
edge4

## Slide 6
Chart: Experiment2 %CPU Utilisation
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 40
Edge1 (Receiver) | 0.24016 | 0.49338 | 0.44174 | 0.67191 | 0.75581 | 0.92244 | 0.87771 | 0.98925 | 0.97351 | 0.98599 | 1 | 0.98215 | 0.94663 | 0.93857 | 0.9641 | 0.9042 | 0.90152 | 0.93934
Edge4 (Sender) | 0.055673 | 0.01363 | 0.027261 | 0.025533 | 0.028412 | 0.024957 | 0.035899 | 0.083701 | 0.22039 | 0.21616 | 0.20177 | 0.20253 | 0.19927 | 0.20484 | 0.21386 | 0.19255 | 0.19274 | 0.21616
Edge5 (Receiver) | 0.21712 | 0.40603 | 0.50854 | 0.68862 | 0.75581 | 0.88136 | 0.94145 | 0.98176 | 0.97658 | 0.98618 | 0.96583 | 0.976 | 0.98503 | 0.98579 | 0.9975 | 0.92878 | 0.94145 | 0.97677
Saturated point of Edge1 & Edge5
~ 15 Mbps

## Slide 7
Chart: Experiment2 Bit rate
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 40
 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 15.9 | 16 | 16 | 15.3 | 15 | 14.8 | 14.9 | 13.8 | 13.7 | 15.1
Saturated ~ 15 Mbps
143 MBytes 16 Mbits/sec 16 Mbits/sec 0.000 ms 0/103590 (0%) sender

## Slide 8: Suggested Experiment

## Slide 9
Super Edge
Edge1
(Server)
Edge5
(Server)
CPU Utilization of Edge1 &2
Iperf3 log
edge1
Iperf3 log
edge5
Data plane
Control plane
UDP packets
Iperf3 –u –b [2, 4 , 6 ,..., 40M] –t 75
Streaming %CPU info 20 points for every bitrate parameters
Edge4
(Client)
Iperf3 log
edge4
Edge2
(Server)
Iperf3 log
edge2