## Slide 1
Experiment1
Experiment2

## Slide 2: Experiment1
Super Edge
Edge1
(Client)
Edge2
(Server)
CPU Utilization of Edge1 &2
Iperf3 log
edge1
Iperf3 log
edge2
Data plane
Control plane
Edge1 & Edge2 keep streaming CPU utilization info through socket program over the control plane
UDP packets
Iperf3 –u –b [2, 4 , 6 ,..., 40M] –t 75
Streaming %CPU info 20 points for every bitrate parameters

## Slide 3
Chart: Experiment1 Bit rate
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40
Edge1 (sender) | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 27.2 | 28.6 | 29.4 | 27.8 | 28 | 27.4
Edge2 (Receiver) | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 27.2 | 28.6 | 29.4 | 27.7 | 28 | 27.3
Saturated point
~ 28 Mbps

## Slide 4
Chart: Experiment1 %CPU Utilisation
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40
Edge1 (sender) | 0.03299 | 0.052501 | 0.04381 | 0.048954 | 0.035296 | 0.043278 | 0.046293 | 0.042746 | 0.041504 | 0.047357 | 0.048244 | 0.05392 | 0.052501 | 0.095424 | 0.18659 | 0.17506 | 0.18162 | 0.18801 | 0.16885 | 0.19262
Edge2 (receiver) | 0.17559 | 0.33469 | 0.35154 | 0.46045 | 0.57769 | 0.66353 | 0.73093 | 0.78538 | 0.86343 | 0.91274 | 0.94856 | 0.95708 | 0.98528 | 0.99823 | 0.96985 | 0.99503 | 1 | 0.96187 | 0.97978 | 0.98812
Saturated point of Edge2
~ 28 Mbps

## Slide 5: Experiment2
Super Edge
Edge1
(Server)
Edge5
(Server)
CPU Utilization of Edge1 &2
Iperf3 log
edge1
Iperf3 log
edge5
Data plane
Control plane
UDP packets
Iperf3 –u –b [2, 4 , 6 ,..., 40M] –t 75
Streaming %CPU info 20 points for every bitrate parameters
Edge4
(Client)
Iperf3 log
edge4

## Slide 6
Chart: Experiment2 %CPU Utilisation
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 40
Edge1 (Receiver) | 0.24016 | 0.49338 | 0.44174 | 0.67191 | 0.75581 | 0.92244 | 0.87771 | 0.98925 | 0.97351 | 0.98599 | 1 | 0.98215 | 0.94663 | 0.93857 | 0.9641 | 0.9042 | 0.90152 | 0.93934
Edge4 (Sender) | 0.055673 | 0.01363 | 0.027261 | 0.025533 | 0.028412 | 0.024957 | 0.035899 | 0.083701 | 0.22039 | 0.21616 | 0.20177 | 0.20253 | 0.19927 | 0.20484 | 0.21386 | 0.19255 | 0.19274 | 0.21616
Edge5 (Receiver) | 0.21712 | 0.40603 | 0.50854 | 0.68862 | 0.75581 | 0.88136 | 0.94145 | 0.98176 | 0.97658 | 0.98618 | 0.96583 | 0.976 | 0.98503 | 0.98579 | 0.9975 | 0.92878 | 0.94145 | 0.97677
Saturated point of Edge1 & Edge5
~ 15 Mbps

## Slide 7
Chart: Experiment2 Bit rate
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 40
 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 15.9 | 16 | 16 | 15.3 | 15 | 14.8 | 14.9 | 13.8 | 13.7 | 15.1
Saturated ~ 15 Mbps
143 MBytes 16 Mbits/sec 16 Mbits/sec 0.000 ms 0/103590 (0%) sender

## Slide 8: Suggested Experiment

## Slide 9
Super Edge
Edge5
(Server)
Edge1
(Server & Client)
CPU Utilization of Edge1 &2
Iperf3 log
edge5
Iperf3 log
edge1
Data plane
Control plane
UDP packets
Iperf3 –u –b [2, 4 , 6 ,..., 40M] –n 200
Streaming %CPU info 20 points for every bitrate parameters
Edge4
(Client)
Iperf3 log
edge4
Edge6
(Server)
Iperf3 log
edge6

## Slide 10
Chart: Experiment2.2 %CPU Utilisation
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40
Edge1 (Sender & Receiver) | 7.225 | 13.47 | 13.9 | 17.69 | 20.65 | 20.825 | 19.655 | 19.075 | 17.39 | 18.45 | 18.19 | 16.415 | 18.9632 | 17.2444 | 19.54 | 18.215 | 18.3 | 19.015 | 15.93 | 18.1722
Edge4 (Sender x2) | 0.495 | 0.67 | 0.97 | 0.69 | 0.665 | 3.69 | 3.94 | 3.68 | 3.16 | 3.725 | 3.325 | 3.28 | 3.425 | 3.43 | 3.225 | 2.995 | 3.555 | 3.525 | 3.065 | 3.8167
Edge5 (Receiver) | 6.22 | 11.185 | 12.215 | 15.455 | 17.435 | 18.065 | 16.725 | 15.64 | 14.055 | 15.165 | 14.46 | 13.315 | 15.5765 | 14.6833 | 16.105 | 15.36 | 15.685 | 15 | 12.915 | 15.3389
Edge6 (Receiver) | 6.28 | 9.275 | 10.56 | 15.24 | 15.155 | 16.785 | 19.835 | 24.285 | 25.455 | 24.365 | 25.28 | 25.39 | 21.885 | 21.74 | 19.6 | 24.195 | 22.85 | 23.895 | 26.16 | 22.8778

## Slide 11
Chart: Experiment 2.2 bitrate
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40
Edge1 (Receive from Edge4) | 2.02 | 4.05 | 6.03 | 8.06 | 10.1 | 11 | 10.1 | 9.11 | 8.64 | 9.11 | 8.7 | 7.76 | 9.25 | 8.91 | 9.74 | 8.98 | 9.22 | 8.79 | 7.3 | 9.18
Edge4 (Send to Edge1) | 2 | 4 | 6 | 8 | 10 | 10.9 | 10.1 | 9.12 | 8.62 | 9.02 | 8.61 | 7.67 | 9.17 | 8.86 | 9.68 | 8.94 | 9.2 | 8.82 | 7.29 | 9.16
Edge1 (Send to Edge6) | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 17.9 | 16.6 | 17 | 19.2 | 15.6 | 15.5 | 13.3 | 16.7 | 16 | 16.7 | 19.6 | 16.5
Edge4 (Send to Edge5) | 2 | 4 | 6 | 8 | 10 | 10.9 | 10.1 | 9.12 | 8.62 | 9.02 | 8.61 | 7.68 | 9.17 | 8.87 | 9.68 | 8.93 | 9.25 | 9.08 | 7.36 | 9.24
Edge5 (Receive from Edge4) | 2.02 | 4.05 | 6.03 | 8.06 | 10.1 | 11 | 10.1 | 9.12 | 8.65 | 9.11 | 8.7 | 9.3 | 9.26 | 8.92 | 9.74 | 8.97 | 9.3 | 8.97 | 7.41 | 9.3
Edge6 (Receive from Edge1) | 2.02 | 4.04 | 6.03 | 8.08 | 10.1 | 12.1 | 14.1 | 16.1 | 17.9 | 16.6 | 17 | 18.9 | 15.7 | 15.5 | 13.3 | 16.8 | 16 | 16.9 | 19.8 | 16.5

## Slide 12
Super Edge
Edge1
(Client)
CPU Utilization of Edge1 &2
Iperf3 log
edge1
Data plane
Control plane
UDP packets
Iperf3 –u –b [2, 4 , 6 ,..., 20M] –t 90 or 75
Streaming %CPU info 20 points for every bitrate parameters
Edge4
(Client)
Iperf3 log
edge4

## Slide 13
Super Edge
Edge1
(Client)
CPU Utilization of Edge1 &2
Iperf3 log
edge1
Data plane
Control plane
Edge 4 UDP packets
Iperf3 –u –b [2, 4 , 6 ,..., 20M] –t 90 or 75
Streaming %CPU info 20 points for every bitrate parameters
Edge4
(Client)
Iperf3 log
edge4
Edge1 UDP packets
Iperf3 –u –b 15M –t 90 or 75

## Slide 14
Chart: Experiment3: %CPU Utilisation when edge1's bitrate is fixed as 15 Mpbs
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
Edge1 (sender & receiver) | 26.64 | 27.525 | 28.355 | 27.92 | 28.635 | 29.0125 | 30.1333 | 29.35 | 29.7 | 28.2667
edge2 (sender) | 6.51 | 10.05 | 12.26 | 15.545 | 18.3312 | 22.0125 | 25.1 | 27.2667 | 27.65 | 27.85

## Slide 15
Chart: Iperf Log (Fixed Edge1 as 15Mbps)
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
Superedge (Received from Edge1) | 15.7 | 15.7 | 15.7 | 13.6 | 12.2 | 10.6 | 8.57 | 7.64 | 7.17 | 7.35
Superedge (Received from Edge4) | 2.1 | 4.19 | 6.29 | 7.1 | 7.74 | 7.7 | 7.39 | 7.43 | 7.34 | 7.41
edge1 (sender) | 15.7 | 15.7 | 15.7 | 15.7 | 15.7 | 15.7 | 15.7 | 15.7 | 15.7 | 15.7
edge4 (sender) | 2.1 | 4.19 | 6.29 | 8.39 | 10.5 | 12.6 | 14.7 | 16.8 | 18.9 | 21

## Slide 16
Chart: SUM Receiving bitrate2 4 6 8 10 12 14 16 18 20
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
 | 17.8 | 19.89 | 21.99 | 20.7 | 19.94 | 18.3 | 15.96 | 15.07 | 14.51 | 14.76

## Slide 17
Super Edge
Edge1
(Client)
CPU Utilization of Edge1 &2
Iperf3 log
edge1
Data plane
Control plane
Streaming %CPU info 20 points for every bitrate parameters
Edge4
(Client)
Iperf3 log
edge4
Edge4 UDP packets
Iperf3 –u –b 15M –t 90 or 75
Edge 1 UDP packets
Iperf3 –u –b [2, 4 , 6 ,..., 20M] –t 90 or 75

## Slide 18
Chart: Experiment3: %CPU Utilisation when edge4's bitrate is fixed as 15 Mpbs
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
Edge1 (sender & receiver) | 25.05 | 25.97 | 26.7467 | 27.4 | 28.2 | 28.55 | 29.3889 | 29.975 | 30.9923 | 31.4
edge2 (sender) | 26.46 | 26.2158 | 26.35 | 25.6375 | 26.32 | 26.12 | 26.2889 | 26.9 | 27.1667 | 27

## Slide 19
Chart: Iperf Log (Fixed Edge4 as 15Mbps)
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
Superedge (Received from Edge1) | 1.8 | 3.35 | 4.53 | 5.83 | 6.36 | 7.19 | 8.24 | 7.73 | 8.04 | 7.97
Superedge (Received from Edge4) | 13.2 | 12 | 10.5 | 10.1 | 8.68 | 8.29 | 7.75 | 6.83 | 7.08 | 7.03
edge1 (sender) | 2.1 | 4.19 | 6.29 | 8.39 | 10.5 | 12.6 | 14.7 | 16.8 | 18.9 | 21
edge4 (sender) | 15.7 | 15.7 | 15.7 | 15.7 | 15.7 | 15.7 | 15.7 | 15.7 | 15.7 | 15.7